## Slide 1
MIRAGE · CROSS-EMBODIMENT
Panda → xArm7
Simulation Policy Transfer
현재 실험 세팅 · 전이 파이프라인 · 정량 검증
PickPlaceCan + Lift | Robosuite 1.4.1 | low-dimensional policy
TARGET SUCCESS PickPlaceCan step 116
2026.08.10 · local working tree

## Slide 2
한 줄 결론
정책 실행 주체와 성공 판정 주체를 분리해 xArm7 전이를 검증
02
정책은 Panda에서 실행하고, 성공은 xArm7에서 판정했다.
동일한 저차원 체크포인트 출력을 Panda 시뮬레이터에서 1 step 실행한 뒤, 달성 pose를 변환·검증하여 xArm7이 절대 pose로 추종한다.
의미 로봇 형태가 달라도 task-space pose contract로 실행 경로를 분리
현재 결과는 실제 로봇이 아닌 시뮬레이션 검증이다.
1 / 1
PickPlaceCan
target step 116 contact-relaxed steps 32
4 / 4
Lift
seeds 0, 1, 3, 7 target step 41–57
0
실패 이벤트
timeout 0 iteration limit 0 rejection 0
검증 현재 작업 트리 회귀 테스트 87 passed
Local working tree · 2026-08-10 · SIMULATION ONLY
sources: task-aware rollout reports + pytest

## Slide 3
실험 세팅
source policy와 target control environment를 완전히 분리
03
SOURCE
Franka Emika Panda
Robosuite robot id: Panda
• 저차원 robomimic checkpoint
• action: [Δp(3), Δrotvec(3), gripper]
• OSC_POSE · control_delta=true · 20 Hz
• checkpoint action + 1 physics step
• camera / offscreen rendering disabled
panda_sim_world
TARGET
xArm7
in-process Robosuite target
• policy camera를 상속하지 않는 control env
• absolute blocking OSC_POSE
• target task success로만 early stop
• workspace / joint / freshness safety gate
• gripper: −1 open, +1 closed
xarm7_sim_world
pose contract
범위 SIMULATION ONLY · ROS command / xArm SDK / robot IP / real calibration 사용 안 함
Local working tree · 2026-08-10 · SIMULATION ONLY
source: xarm_transfer_sim.example.yaml

## Slide 4
End-to-end 실행 파이프라인
온라인 oracle과 learned Ridge가 같은 계약·안전 계층을 공유
04
01
Checkpoint
raw action + metadata
02
Panda step
one policy step + achieved pose
03
Transform v2
task world × tool frame
04
Dynamics
online oracle or Ridge
05
Safety gate
fresh · finite workspace · joints
06
xArm7 OSC
absolute blocking + outer loop
07
Target success
task event terminates
Provider만 교체 oracle: Panda achieved next pose | Ridge: autoregressive predicted pose
achieved pose feedback
같은 frame·unit·timestamp contract와 fail-closed validation을 모든 단계에서 유지
Local working tree · 2026-08-10 · SIMULATION ONLY
source: rollout.py · contracts.py · runtime.py

## Slide 5
좌표 변환 v2
task/world 정합과 tool convention을 분리해 motion direction 왜곡을 방지
05
TtargetWorld,targetTool = TtargetWorld,sourceWorld @ TsourceWorld,sourceTool @ TsourceTool,targetTool
LEFT-MULTIPLY
Task / world transform
Panda와 xArm7이 동일한 task 좌표를 사용
현재 값 IDENTITY
translation = [0, 0, 0] m rotation = [0, 0, 0, 1] XYZW
RIGHT-MULTIPLY
Tool-frame correction
nominal gripper axis 차이만 local-Z에서 보정
현재 값 −90° about local Z
quaternion = [0, 0, −0.7071, 0.7071]
핵심 home pose로 변환을 추정하지 않으며, simulation transform을 real calibration으로 표시할 수 없다.
Local working tree · 2026-08-10 · SIMULATION ONLY
source: simulation_transform.py · transform version 2

## Slide 6
Target control & safety
absolute blocking OSC에 보상 루프와 task-aware 예외를 제한적으로 적용
06
ADMISSION GATES
Frame / type
simulation_only · xarm7_sim_world
Freshness
age ≤ 0.15 s · future skew ≤ 0.02 s
Workspace
[−0.65,−0.60,0.40]–[0.35,0.60,1.35] m
Joint limits
model limit + 0.01 rad margin
Learned model
held-out position / orientation bounds
BLOCKING OSC
Free-space convergence
2.5
cm
position tol.
7°
orientation
tolerance
• 5 consecutive in-bound steps
• position correction ≤ 3 cm
• orientation correction ≤ 5°
• timeout 2 s · max 300 iterations
CONTACT EXCEPTION
PickPlaceCan only
simulator가 gripper ↔ Can 접촉을 직접 확인한 동안만
6.0 cm / 18°
• Kp = [300,300,500,300,300,300]
• position compensation ≤ 10 cm
• Lift에서는 항상 비활성
• workspace/joint/freshness gate는 유지
Target task-success event가 발생하면 마지막 EE pose가 미수렴이어도 즉시 종료
Local working tree · 2026-08-10 · SIMULATION ONLY
source: profiles.py · control.py

## Slide 7
평가 프로토콜
task profile이 checkpoint·observation·controller를 정적으로 고정
07
TASK 01
PickPlaceCan
• object obs [14] · graspable Can
• checkpoint: can / low_dim / epoch 250
• native horizon 400 · full task seed 1
• contact relaxation enabled
TASK 02
Lift
• object obs [10] · graspable cube
• checkpoint: lift / low_dim / epoch 1000
• native horizon 400 · seeds 0,1,3,7
• contact relaxation disabled
PROVIDERS
online_oracle
Panda achieved next pose를 즉시 사용
learned_ridge
recorded action을 autoregressive replay
DATASET
300 transitions
train: seeds 0,2,4,5 (200) validation: seeds 1,3 (100) whole-episode split · seed 11
RUNTIME CONTRACT
low_dim만 실행 가능
image modes: classified, fail closed
unregistered task: fail closed
Lift Ridge training: 현재 범위 밖
Local working tree · 2026-08-10 · SIMULATION ONLY
source: profiles.py · dataset/model reports

## Slide 8
Forward dynamics: held-out one-step prediction
episode leakage 없이 100개 validation transition으로 비교
08
2.39 mm
Ridge position RMSE
α = 0.01 · selected deployable model
0.254°
Ridge orientation RMSE
held-out one-step prediction
≈75%↓ position RMSE
Ridge vs. identity baseline 9.63 mm → 2.39 mm
주의: one-step held-out error는 50-step autoregressive drift의 online safety bound가 아니다.
Local working tree · 2026-08-10 · SIMULATION ONLY
source: forward_dynamics_evaluation.json

## Slide 9
50-step xArm7 tracking: Oracle vs. Ridge
동일 held-out seeds 1·3·7, 같은 transform·controller·safety stack
09
6 / 6
rollouts complete
Oracle 3 + Ridge 3 all 50 / 50 steps
0
control failures
timeout · iteration limit rejection · contact event
Ridge도 target tracking 유지
mean pos 0.49–0.89 cm mean ori 1.02–2.17°
그래프는 controller가 달성한 target tracking mean error; learned source-pose drift와 분리해 보고
Local working tree · 2026-08-10 · SIMULATION ONLY
source: task_tool_v2 oracle / learned rollout reports

## Slide 10
Full-task 결과 ① PickPlaceCan
xArm7가 can을 집어 bin에 놓는 실제 task event로 성공 판정
10
STEP 1 · approach
STEP 31 · pre-grasp
STEP 61 · grasp
STEP 116 · TARGET SUCCESS
SEED 1
116 / 400
policy steps until target success
• timeout 0 · iteration limit 0
• safety rejection 0
• verified-contact steps 32
• mean command latency 38.6 ms
• target-only early termination
final task event > pose convergence
성공 시점의 큰 EE residual은 object contact / immediate task-success 규칙으로 별도 기록됨
Local working tree · 2026-08-10 · SIMULATION ONLY
source: panda_xarm_oracle_seed1_full_task.mp4 + report

## Slide 11
Full-task 결과 ② Lift
모든 seed에서 target success까지 계속 실행; contact relaxation은 사용하지 않음
11
4 / 4
target success
seeds 0 · 1 · 3 · 7
≤ 2.07 cm
maximum position error
all four full-task rollouts
0 failures
timeout · iteration limit rejection · contact tolerance
seed 1: Panda success step 40 → xArm7 success step 41; source success가 target rollout을 조기 종료하지 않음
Local working tree · 2026-08-10 · SIMULATION ONLY
source: lift/low_dim/xarm_rollout_report.json

## Slide 12
재현 방법
task-aware CLI가 checkpoint에서 task·mode·native horizon을 해석
12
RUN
cd mirage MUJOCO_GL=egl ../.venv/bin/python -m \ mirage.benchmark.robosuite.xarm_transfer.cli rollout \ --checkpoint mirage/models/can/low_dim/\ model_epoch_250_PickPlaceCan_success_1.0.pth \ --mode oracle --seeds 1 --terminate-on-success
VERIFY
PYTEST_DISABLE_PLUGIN_AUTOLOAD=1 PYTHONPATH=... \ python -m pytest -q --import-mode=importlib \ test_xarm_transfer_*.py test_canonical_policy_checkpoint.py
ENVIRONMENT
• Ubuntu 22.04.5 · Python 3.10.12
• Robosuite 1.4.1 · MuJoCo 2.3.2
• ROS 2 Humble installed, unused in rollout
• RTX 5060 Laptop GPU · EGL rendering
• branch: agent/xarm7-development
• HEAD: 4e4429e + local working tree
VALIDATION
87 passed in 70.81 s
current working tree · 2026-08-10 results stay under ignored results/
Local working tree · 2026-08-10 · SIMULATION ONLY
source: CLI README + local validation

## Slide 13
결론 및 다음 단계
현재 성과와 경계 조건을 함께 제시
13
현재 확보한 것
• Panda policy → xArm7 control의 명시적 contract
• task/world와 tool-frame을 분리한 transform v2
• PickPlaceCan 1/1, Lift 4/4 target success
• Oracle/Ridge 50-step 6/6 completion
• 87개 회귀·통합 테스트 통과
아직 주장하지 않는 것
• 실제 xArm7 hardware 성공
• real-world calibration
• image observation runtime
• Lift learned Ridge model
• Stack/Square/Assembly 지원
NEXT
1. real calibration 경로를 별도 구현
2. low-speed fake → real safety gate
3. image observation / cross-painting 연결
4. Lift용 dynamics dataset·Ridge 학습
5. multi-seed PickPlaceCan 확대
Takeaway · embodiment 차이는 pose contract로 흡수하고, 안전·성공 판정은 target에서 닫는다.
Local working tree · 2026-08-10 · SIMULATION ONLY
Mirage xArm7 simulation transfer